Abstract

LiSA stands for Linux Switch Appliance. It's an entirely open‑source project that aims at delivering a cheap and efficient solution to small‑sized networks. LiSA implements both Layer 2 and Layer 3 packet switching. At the same time, it has advanced configuration and monitoring features. Based on the Linux Operating System, packet switching is entirely accomplished in software. As opposed to a hardware implementation, LiSA aims at providing advanced features rather than high bandwidth and low latency. Being based on the Linux Kernel, LiSA can run on any architecture supported by this kernel; no specialized hardware is required. As an open‑source project, it is also a great learning platform for those who wish to study Layer 2 and Layer 3 protocols and algorithms. This paper contains a brief presentation of LiSA's currently implemented features, a comparison between LiSA and existing Linux Kernel modules that aim at similar functionality, detailed description of LiSA's architecture and kernel integration, a few words about the Linux Kernel RX stack, and results of our own performance tests.

# LiSA Features Overview
# LiSA vs. Bridge + 8021q
## Port Trunk with Bridge + 8021q Example
# User Space Architecture
# Kernel Space Architecture
## Minimum Data Copy Optimization
## Packet "Post‑Processing"
# A Few Words about the Linux Kernel RX Stack
The RX Stack is the set of functions that handles packet reception from the physical network interface and delivery to higher level protocol processing routines. The RX Stack can be logically divided into two parts: low‑level hardware routines and kernel RX framework. Although no strict specifications exists for the low‑level parts (except for the driver API that is used by the RX framework), drivers tend to follow existing guidelines and recommendations. The kernel RX framework is responsible for separating the low‑level routines and the packet processing logic. Device driver developers need not worry about when packets are scheduled to be processed and how they are processed. This is all taken care of by the RX framework. Protocol developers need not worry about how packets are received from the hardware, because this is also taken care of by the RX framework (and the underlaying drivers).
Two driver frameworks coexist in current (2.6) kernel versions: SoftNET and NAPI. The former was widely used in early 2.4 kernels and nowadays it's nothing but a compatibility hack that provides compatibility with older driver. The latter was added in late 2.4 kernels and is the preferred (and standard) framework for 2.6 kernels, because of its great features. The two frameworks are different only in the RX (and not the TX) part.
I'll briefly explain the NAPI RX framework[1], using the (simple) 8139too driver as an example.
[1] Detailed descriptions of both SoftNET and NAPI can be found in the full LiSA paper available on http://lisa.ines.ro/.
## Generic and Protocol‑Specific Handlers
## Packet "Post-Processing"
# Performance