Abstract

LiSA stands for Linux Switch Appliance. It's an entirely open‑source project that aims at delivering a cheap and efficient solution to small‑sized networks. LiSA implements both Layer 2 and Layer 3 packet switching. At the same time, it has advanced configuration and monitoring features. Based on the Linux Operating System, packet switching is entirely accomplished in software. As opposed to a hardware implementation, LiSA aims at providing advanced features rather than high bandwidth and low latency. Being based on the Linux Kernel, LiSA can run on any architecture supported by this kernel; no specialized hardware is required. As an open‑source project, it is also a great learning platform for those who wish to study Layer 2 and Layer 3 protocols and algorithms. This paper contains a brief presentation of LiSA's currently implemented features, a comparison between LiSA and existing Linux Kernel modules that aim at similar functionality, detailed description of LiSA's architecture and kernel integration, a few words about the Linux Kernel RX stack, and results of our own performance tests.

# LiSA Features Overview
LiSA currently implements Layer 2 and Layer 3 packet switching. The central point for control and management is a user space command line interface (CLI). It was designed to ressemble as close as possible Cisco's IOS CLI.
Full 802.1q support is implemented, including a VLAN database, port trunks and list of allowed VLANs. Because it was meant as an IOS clone, the IOS approach to VLAN assignment is used:
- VLANs are assigned to ports, using a port‑centric configuration;
- ports have two VLAN-operating modes: access (untagged) and trunk (802.1q tagged);
- each trunk port has a list of allowed VLANs.
VLAN management was adapted from late versions of IOS: it's handled through the config/vlan prompt rather than an entirely separate configuration area called "VLAN Database".
At Layer 2, no support for STP, CDP and IGMP snooping is currently available (although we plan to implement these during the next months).
At Layer 3, only simple packet routing (i.e. using the existing kernel routing code) is supported, with no routing management available through the command line interface. Access lists, policy maps and routing protocols are not implemented (although further development is expected, which should include such features). Similar to the IOS, VLAN‑specific virtual interfaces can be dinamically created. Layer 3 addresses can be assigned to these virtual interfaces, and thus inter‑VLAN routing occurs naturally.
# LiSA vs. Bridge + 8021q
Judging by its currently implemented features, one could easily state that LiSA is useless, because similar functionality can be achieved with two existing kernel modules, if they are cleverly used together. The two modules are bridge and 8021q.
The bridge module combines several network devices into a classic switch. It also provides a virtual interface, which can be assigned an ip address. To the bridge, the virtual interface is just another port. To the host, the virtual interface acts like a physical interface connected to one of the switch's ports.
The 8021q module turns a network device into a VLAN‑aware interface. One virtual interface is created for each VLAN. Each virtual interface sends and receives untagged packets. When these packets are sent or received through the network device, 8021q tags are appropriately processed, so that packets apear to be untagged on the virtual interfaces.
## Port Trunk with Bridge + 8021q Example
As we stated earlier, similar functionality can be achieved with two existing kernel modules, if they are cleverly used together. Here's a short, eloquent example:
Suppose we had a machine with 4 network interfaces, and we wanted to configure these interfaces as follows:
- eth0 in trunk mode, allowing access to VLANs 1 and 2;
- eth1 in trunk mode, allowing access to VLANs 1 and 3;
- eth2 in access mode, in VLAN 2;
- eth3 in access mode, in VLAN 3.
Additionally, routing must be accomplished between VLANs 2 and 3, using address 192.168.2.254/24 on VLAN 2 and address 192.168.3.254/24 on VLAN 3.
The command sequence that builds up this configuration is:
modprobe bridge
modprobe 8021q

vconfig set_name_type DEV_PLUS_VID_NO_PAD
vconfig add eth0 1
vconfig add eth0 2
vconfig add eth1 1
vconfig add eth1 3

brctl addbr br1
brctl addif br1 eth0.1
brctl addif br1 eth1.1

brctl addbr br2
brctl addif br2 eth0.2
brctl addif br2 eth2

brctl addbr br3
brctl addif br3 eth1.3
brctl addif br3 eth3

ifconfig br2 192.168.2.254 netmask 255.255.255.0
ifconfig br3 192.168.3.254 netmask 255.255.255.0

ifconfig eth0 up
ifconfig eth1 up
ifconfig eth2 up
ifconfig eth3 up
This approach has two major drawbacks:
- One virtual interface is necessary for each VLAN in each trunk mode port. If all 4094 VLANs must be switched between two trunk ports, a total of 8188 virtual interfaces are needed for VLAN support only.
- When a packet is flooded / multicast and both trunk mode and access mode ports are involved, the same tagging / untagging operations take time several times. This also implies additional overhead with socket buffer operations.
LiSA uses its own kernel module to accomplish these tasks. Since it was meant for an inteligent Layer 2 switch as a whole right from the beginning, several optimizations have been made to mitigate these drawbacks:
- LiSA needs no virtual interfaces at all to handle per‑VLAN packet switching.
- When a packet is flooded / multicast, ports are "re‑ordered" so that a minimum number of socket buffer operations are performed.
Virtual interfaces are still used to provide compatibility with existing Layer 3 code and thus allow for easy inter‑VLAN routing. However, these interfaces were designed in such a manner that they have minimum overhead (basically they just add a few more stack levels).
# User Space Architecture
Right from the beginning, LiSA was designed having dedicated systems in mind. Ideally, embedded systems should be used, but this does not mean it cannot run on standard PC architectures. Because of the dedicated systems idea, several flavors of CLI were designed:
The swcon binary is meant to be indirectly spawn by init (by the means of an agetty or similar program). Ideally, it would be spawn on a serial port to resemble a dedicated switch's serial console.
The swclid daemon is a very light version of the famous inetd daemon. It only listens on a single TCP port (usually telnet) and indirectly (by the means of in.telnetd) spawns the swlogin binary.
The swcli binary directly opens a highest privilege level CLI. It's mostly meant for testing purposes or shared (i.e. not dedicated) hosts.
Because all binaries must provide the same functionality once authentication is completed, all CLI functionality is actually implemented in a common library (object) rather than the binaries themselves.
Because several management sessions (CLI instances) can run simultaneously, configuration must be shared between them. All switching control and configuration data is kept in kernel space, and thus it's shared by default. However, several pieces of information (such as the user and enable passwords) are not fitted to be stored in kernel space. Instead, IPC mechanisms are used to serve this purpose. A shared memory segment is used to store shared information in userspace. Additionaly, a semaphore ensures consistent access to the shared memory segment.
# Kernel Space Architecture
## Minimum Data Copy Optimization
## Packet "Post‑Processing"
# A Few Words about the Linux Kernel RX Stack
The RX Stack is the set of functions that handles packet reception from the physical network interface and delivery to higher level protocol processing routines. The RX Stack can be logically divided into two parts: low‑level hardware routines and kernel RX framework. Although no strict specifications exists for the low‑level parts (except for the driver API that is used by the RX framework), drivers tend to follow existing guidelines and recommendations. The kernel RX framework is responsible for separating the low‑level routines and the packet processing logic. Device driver developers need not worry about when packets are scheduled to be processed and how they are processed. This is all taken care of by the RX framework. Protocol developers need not worry about how packets are received from the hardware, because this is also taken care of by the RX framework (and the underlaying drivers).
Two driver frameworks coexist in current (2.6) kernel versions: SoftNET and NAPI. The former was widely used in early 2.4 kernels and nowadays it's nothing but a workaround that provides compatibility with older drivers. The latter was added in late 2.4 kernels and is the preferred (and standard) framework for 2.6 kernels, because of its great features. The two frameworks are different only in the RX (and not the TX) part.
I'll briefly explain the NAPI RX framework[1], using the (simple) 8139too driver as an example.
[1] Detailed descriptions of both SoftNET and NAPI can be found in the full LiSA paper available on http://lisa.ines.ro/.
## Generic and Protocol‑Specific Handlers
## Packet "Post-Processing"
# Performance